## Slide 1: Computer Organization and Assembly Language (CS2523)
Department of Computer Science,
Capital University of Science and Technology, Islamabad
Fall Semester, 2022

## Slide 2: Lecture Outlines
Microprocessor Systems (Intro & History)
Evolution of Microprocessors
Moore’s Law
Introduction to Computer Organization
Introduction to Assembly – Translating Languages

## Slide 3: Where this course fits in

## Slide 4: A Short List of Microprocessor Systems
Digital Computers
Digital Camera
Digital television
Digital audio & video players
Cell phones
Modern radios
Digital calculators
Medical equipments
Communication Equipments
Control systems

## Slide 5: Main Objectives of Course
Describe the function of each unit inside the microprocessor (Architectural details).
Understand and write code in the Intel Assembly language for the 80xxx family.

## Slide 6: Historical Background
First Generation
  No mechanical components anymore
  Vacuum Tubes
Principle
  Basic: Triode
  Grid voltage (anode) to simply turn a current On / Off (Half wave rectification)
1946: ENIAC machine
  Electronic Numerical Integrator And Computer

## Slide 7: Historical Background
ENIAC

## Slide 8: Historical Background
IAS Machine1952 by von Neumann
  Institute for Advanced Studies computer
  First machine based on machine language(binary)

## Slide 9: Historical Background IAS Machine
Dominant architecture in today’s systems
  Used in all popular systems / chips
Modifications/Up-gradations
  CPU (Central Processing Unit)
  New memory paths between memory and I/O Direct Memory Access (DMA)
New incorporated Ideas
  Multiple arithmetic units / Multiple CPUs (Multicore)
  Parallel processing

## Slide 10: Historical Background
Transistors replaced Vacuum tubes in 1948
  Smaller, more power efficient
  Still large machines
Evolution of Integrated Circuits(IC’s) in 1958
  Many transistors packed on one die
  High density & reliability, low power

## Slide 11: Historical Background
Gen. | Dates | Technology | Speed | Time/Ops
1 | 1946-1957 | Vacuum tube | 40 KHz | 25 µs
2 | 1958-1964 | Transistor | 200 KHz | 5 µs
3 | 1965-1971 | Small and medium integrated circuits | 1 MHz | 1 µs
4 | 1972-1977 | Large scale integration | 10 MHz | 100 ns
5 | 1978- | Very large scale integration | 100 MHz | 10 ns

## Slide 12: Microprocessors Age -- Intel
In 1971
  The world’s 1st microprocessor, the Intel 4004 was introduced
    4-bit microprocessor
    Addresses only 4096 x 4bit memory
    Speed 50k instructions per second

## Slide 13: Example: A thermostat
4-bit microprocessor
A thermostat is a component which senses the temperature of a physical system and performs actions so that the system's temperature is maintained near a desired set point.
Notes: A thermostat is a component which senses the temperature of a physical system and performs actions so that the system's temperature is maintained near a desired set point.

## Slide 14: Microprocessors Age -- Intel
Later in 1971
  8008 was released
  8-bit version of the 4004
  It addressed a 16K byte memory
In 1973
  8080 was introduced
  limitations of the speed and instruction set of 8008 were addressed and improved
  It addressed a 64K bytes memory

## Slide 15: Example: NASA's Mars Sojourner Rover
8-bit microprocessor
  Intel’s 80C85
Notes: Sojourner is the Mars Pathfinder robotic Mars rover that landed on July 4, 1997 in the Ares Vallis region, and explored Mars for around three months. It has front and rear cameras and hardware to conduct several scientific experiments.

## Slide 16: Example: NASA's Mars Sojourner Rover
8-bit microprocessor
  Intel’s 80C85
  Sojourner is the Mars Pathfinder robotic Mars rover that landed on July 4, 1997 in the Ares Vallis region, and explored Mars for around three months. It has front and rear cameras and hardware to conduct several scientific experiments.

## Slide 17: Microprocessors Age -- Intel
In 1978-79
  8086 and 8088 modern µp’s (Microprocessors) were introduced.
  16-bit microprocessors (8 bit external data bus for 8088)
  Addresses 1M byte of memory.
  2.5 million instructions per second
  Multiply and divide instructions included
International Business Machines(IBM) decided to use the 8088 in its first ever PC in 1981 making it very popular

## Slide 18: Microprocessors Age -- Intel
Intel 80x86 Family
  The 80286, 16-bit microprocessor
    Addresses a 16 M byte memory
    Speed4 MIPs
  The 80386 was introduced in 1986
    It was the first 32-bit microprocessor that contained a 32- bit data bus and a 32-bit address bus.
  The 80486 was introduced in 1989
    It had an 8K byte cache memory in addition to being faster than the .386
Million instructions per second (MIPS) is an older, obsolete measure of a computer's speed and power, MIPS measures roughly the number of machine instructions that a computer can execute in one second.
Notes: Million instructions per second (MIPS) is an older, obsolete measure of a computer's speed and power, MIPS measures roughly the number of machine instructions that a computer can execute in one second.

## Slide 19: Microprocessors Age -- Intel
Intel Pentium Microprocessors
  Introduced in 1993
  16K byte Cache Memory
  4G Bytes of Memory Addressing
  Speed150 MIPs
  Data bus width increased to 64-bit
Later Pentium versions are up-gradations of above specifications in terms of Speed, Memory(levels of caches) and more complex instruction set

## Slide 20: Microprocessors Age -- Intel
Intel Pentium Microprocessors
  Introduced in 1993
  16K byte Cache Memory
  4G Bytes of Memory Addressing
  Speed150 MIPs
  Data bus width increased to 64-bit
Later Pentium versions are up-gradations of above specifications in terms of Speed, Memory(levels of caches) and more complex instruction set

## Slide 23: Example: Sony Aibo ERS-110 Robotic Dog
Microprocessor: 64- bit MIPS RISC
What they have in common: They sense the environment (input signals), decide on (compute) their actions (responses) in real time.
RISC (reduced instruction set computer) is a microprocessor that is designed to perform a smaller number of types of computer instructions so that it can operate at a higher speed (perform more millions of instructions per second, or MIPS).
Notes: RISC (reduced instruction set computer) is a microprocessor that is designed to perform a smaller number of types of computer instructions so that it can operate at a higher speed (perform more millions of instructions per second, or MIPS).

## Slide 24: Moore’s Law
Gorden Moore (Co-founder of Intel) observed in 1965 that the number of transistors that could be put on a single chip was doubling every year and predicted that this pace would continue
He later revised the time to 18 months (in 1975) and this rate has sustained since

## Slide 25: Moore’s Law

## Slide 26: Moore’s Law

## Slide 27: Computer Organization
This course is design to understand the basics organization of computers
Address bus - carries memory addresses from the processor to other components such as primary storage and input/output devices. The address bus is unidirectional .

## Slide 28: Computer Organization
Data bus - carries the data between the processor and other components. The data bus is bidirectional .
Control bus - carries control signals from the processor to other components. The control bus also carries the clock's pulses. The control bus is unidirectional.

## Slide 29: Basic Computer Organization
Processor
I/O
Memory

## Slide 30: Basic Computer Organization
Memory Data
Processor
Operation

## Slide 31: Basic Computer Organization
Memory Data
Processor
Operation

## Slide 32: Basic Computer Organization
Memory
Processor
Address Bus
Data Bus
Control Bus

## Slide 33: Dimensions of Memory
Horizontal Dimensions = Width of Memory Cell
Vertical Dimensions
=
Size of
Memory
00000000
00000001
00100011
00100100
00100101
Binary
Addresses
Of
Memory
Cells

## Slide 34: Basic Computer Organization
Memory
Processor
Control Bus

## Slide 35: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language: mov eax,A
mul B add eax,C
call WriteInt
Intel Machine Language: A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 36: Translating Languages
WriteInt PROC
Writes a signed 32-bit decimal number to standard output in decimal format with a leading sign and no leading zeros.
Call args: EAX = signed number to write
Return arg: None
Example:
mov eax,216543
call WriteInt
Output: +216543
NOTES: To write an unsigned integer, use the WriteDec procedure.
To write in hexadecimal, use the WriteHex procedure.
To write in binary, use the WriteBin procedure.
Use the mShow macro to display the contents of an 8-, 16-, or 32-bit variable or register in any combination of hexadecimal, signed decimal, unsigned decimal, or binary formats.
The FUNCTION directive marks the start of a function. PROC is a synonym for FUNCTION.