## Slide 1: Computer Organization and Assembly Language (CS2523)
Department of Computer Science,
Capital University of Science and Technology, Islamabad
Fall Semester, 2022

## Slide 2: Lecture Outlines
Welcome to Assembly Language
Applications of Assembly Language
Assembly Language Comparison
Programmer’s View of a Computer System/ Virtual Machine Concept
General Concepts of a sequential architecture/ Instruction Cycle

## Slide 3: Welcome to Assembly Language(AL)
Oldest programming languages of all languages
Provides direct access to computer hardware
AL programmer knows a great deal about the computer architecture and OS(operating system)

## Slide 4: Welcome to Assembly Language(AL)
Assembler
  A program that converts an AL source code program to machine language
  Popular Assemblers
    MASM (Microsoft Assembler)
    EMU8086 (Microprocessor Emulator)
    TASM (Borland Turbo Assembler)
    NASM (The Netwide Assembler)

## Slide 5: Welcome to Assembly Language(AL)
Software/Hardware Need
  Editor
    Text Editor for creating source files
  Assembler
  Linker
    Linker utility is required to produce executable file using libraries
      E-g; link32.exe
  Debugger
    For debugging/profiling of the program(errors detection/correction)
      CodeView for MASM
      Advanced Full Screen Debugger (AFD) for NASM

## Slide 6: Welcome to Assembly Language(AL)
How does assembly language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?
Notes: Things that are not allowed in Assembly Language are also not allowed in Machin Language. One to One mapping, which means that a program shall have equal lines of code of AL and ML.
Assembly Language is Machine Specific and is not portable. Each Machine will have different AL code.

## Slide 7: Assembly Language Applications
Business application for single platform
Hardware device driver
Business application for multiple platforms
Embedded systems & computer games

## Slide 8: Assembly vs High-Level Languages
Some representative types of applications:

## Slide 9: Programmer’s View of a Computer System A Concept by Tanenbaum Virtual Machine Concept
Application Programs
High-Level Language
Assembly Language
Operating System
Instruction Set
Architecture
Microarchitecture
Digital Logic
Level 0
Level 1
Level 2
Level 3
Level 4
Level 5
Increased level of abstraction
Each level hides the details of the level below it

## Slide 10: Programmer's View
Application Programs (Level 5)
  Written in high-level programming languages
  Such as Java, C++, Pascal, Visual Basic . . .
  Programs compile into assembly language level (Level 4)
Assembly Language (Level 4)
  Instruction mnemonics are used
  Have one-to-one correspondence to machine language
  Calls functions written at the operating system level (Level 3)
  Programs are translated into machine language (Level 2)
Operating System (Level 3)
  Provides services to level 4 and 5 programs
  Translated to run at the machine instruction level (Level 2)

## Slide 11: Programmer's View
Instruction Set Architecture (Level 2)
  Specifies how a processor functions
  Machine instructions, registers, and memory are exposed
  Machine language is executed by Level 1 (microarchitecture)
Microarchitecture (Level 1)
  Controls the execution of machine instructions (Level 2)
  Implemented by digital logic (Level 0)
Digital Logic (Level 0)
  Implements the microarchitecture
  Uses digital logic gates
  Logic gates are implemented using transistors
Notes: A microarchitecture is a hardware implementation of an ISA (instruction set architecture)
The MicroArchitecture of a processor specifies the details regarding the implementation of features specified in its ISA.
An example can be: The ISA could have exposed an instruction like “ADD”, MicroArchitecture gives the details about how this particular instruction is designed within the processor.

## Slide 12: Assembly and Machine Language
Machine language
  Native to a processor: executed directly by hardware
  Instructions consist of binary code: 1s and 0s
Assembly language
  Slightly higher-level language
  Readability of instructions is better than machine language
  One-to-one correspondence with machine language instructions
Assemblers translate assembly to machine code
Compilers translate high-level programs to machine code
  Either directly, or
  Indirectly via an assembler

## Slide 13: Compiler and Assembler

## Slide 14: Translating Languages
English: D is assigned the sum of A times B plus 10.
High-Level Language: D = A * B + 10
Intel Assembly Language:
mov eax, A
mul B
add eax, 10
mov D, eax
Intel Machine Language:
A1 00404000
F7 25 00404004
83 C0 0A
A3 00404008
A statement in a high-level language is translated typically into several machine-level instructions

## Slide 15: Translating Languages
These are called instructions, and they specify operations that are to be performed by the processor.
mov is a mnemonic for move,
while mul is a mnemonic for multiply.
Other common instructions include add, sub, and div.
I trust you can figure out what operation these specify!

## Slide 16: Translating Languages
Most instructions take two parameters.
In the technical jargon, these are often known as operands.
The first (on the left) is the destination,
and the second (on the right) is the source.
So, in the case of mov bx, 5
this moves the literal value 5 into the destination register bx. The order of these parameters matters, of course, because you could not move the contents of the register bx into the literal value 5!

## Slide 17: Translating Languages
The mul instruction is a little bit strange because some of its operands are implicit.
That is, they are not explicitly specified as parameters.
For the mul instruction,
  the destination operand is hard-coded as the ax register.
  The source operand is the one that you pass as a parameter: it can be either a register or a memory location.

## Slide 18: Translating Languages
Therefore, you could imagine that mul cx means
mul ax, cx
but you don't write it that way because the ax destination register is implicit.
Now, a mul instruction commands the processor to multiply the destination operand by the source operand, and store the result in the destination. In code, you can imagine that mul cx would translate into ax = ax * cx.

## Slide 19: Translating Languages
If you want to do 5 * 10, then:
mov ax, 5 ; ax = 5
mov cx, 10 ; cx = 10
mul cx ; ax = ax * cx

## Slide 20: Translating Languages-Registers
Modern (i.e x86 and beyond) x86 processors have eight 32-bit general purpose registers, as depicted in Figure:

## Slide 21: Translating Languages-Registers
The register names are mostly historical.
For example, EAX used to be called the accumulator since it was used by a number of arithmetic operations, and
ECX was known as the counter since it was used to hold a loop index.
Whereas most of the registers have lost their special purposes in the modern instruction set, by convention, two are reserved for special purposes — the stack pointer (ESP) and the base pointer (EBP).

## Slide 22: Translating Languages-Registers
For the EAX, EBX, ECX, and EDX registers, subsections may be used. For example, the least significant 2 bytes of EAX can be treated as a 16-bit register called AX. The least significant byte of AX can be used as a single 8-bit register called AL, while the most significant byte of AX can be used as a single 8-bit register called AH. These names refer to the same physical register.
When a two-byte quantity is placed into DX, the update affects the value of DH, DL, and EDX. These sub-registers are mainly hold-overs from older, 16-bit versions of the instruction set. However, they are sometimes convenient when dealing with data that are smaller than 32-bits (e.g. 1-byte ASCII characters).

## Slide 23: Translating Languages-Registers
When referring to registers in assembly language, the names are not case-sensitive. For example, the names EAX and eax refer to the same register.

## Slide 24: General Concepts
Basic Microcomputer Design
registers
data bus
Central Processor Unit (CPU)
Memory Storage Unit
I/O Device #1
I/O Device #2
control bus
address bus
ALU | CU | clock

## Slide 25: Basic Architecture
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Registers
IR
PC
Memory
I/O

## Slide 26: Datapath Operations
  Load
– Read memory location into register
ALU operation
– Input certain registers through ALU, store
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
+1
back in register
Store
– Write register to memory location
Registers
IR
PC
Memory
I/O
10
11
...
10
.1.1.

## Slide 27: Control Unit
Control unit: configures the datapath operations
– Sequence of desired operations (“instructions”) stored in memory – “program”
Instruction cycle – broken into several sub-operations, each one clock cycle, e.g.:
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Fetch: Get next instruction into IR
Decode: Determine what the instruction means
Fetch operands: Move data from memory to datapath register
Execute: Move data through the ALU
Store results: Write data from register to memory
Registers
IR
PC
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1

## Slide 28: Control Unit Sub-Operations
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Fetch
  Get next instruction into IR
  PC: program counter, always points to next instruction
  IR: holds the fetched instruction
Registers
IR
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1
PC100
load R0, M[500]

## Slide 29: Control Unit Sub-Operations
Decode
– Determine what the instruction means
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Registers
IR
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1
PC100
load R0, M[500]

## Slide 30: Control Unit Sub-Operations
Fetch operands
– Move data from memory to datapath register
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Registers
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1
PC100
load R IR
0, M[500]
10

## Slide 31: Control Unit Sub-Operations
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Execute
  Move data through the ALU
  This particular instruction does nothing during this sub-operation
Registers
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1
PC100
load R IR
0, M[500]
10

## Slide 32: Control Unit Sub-Operations
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Store results
  Write data from register to memory
  This particular instruction does nothing during this sub-operation
Registers
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1
PC100
load R IR
0, M[500]
10

## Slide 33: Instruction Cycles
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Fetch Exec. ops
Store results
clk
PC=100
FetchDecode
Registers
IR
PC
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
R1
10
load R0, M[500]
100

## Slide 34: Instruction Cycles
Processor
Control unit
Datapath
Controller
Control
/Status
PC=100
FetchDecode
Fetch Exec. ops
Store results
clk
ALU
+1
Registers
IR
PC
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
inc R1, R0
10 11
R1
Fetch Exec. ops
Store results
clk
101
PC=101
FetchDecode

## Slide 35
Processor
Control unit
Datapath
Controller
Control
/Status
PC=100
FetchDecode
Fetch Exec. ops
Store results
clk
ALU
+1
IR
PC
Memory
I/O
...
10
...
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
inc R1, R0
10 11
R1
Fetch Exec. ops
Store results
clk
101
PC=101
FetchDecode
Registers

## Slide 36
Processor
Control unit
Datapath
Controller
Control
/Status
PC=100
FetchDecode
Fetch Exec. ops
Store results
clk
ALU
+1
IR
PC
Memory
I/O
...
10
...
500
501
100 mov ax, M[500]
inc bx, ax
store M[501], bx
ax
inc bx, ax
10 11
bx
Fetch Exec. ops
Store results
clk
101
PC=101
FetchDecode
Registers

## Slide 37: Instruction Cycles
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
PC=100
FetchDecode
Fetch Exec. ops
Store results
clk
Registers
IR
PC
Memory
I/O
500
501
100 load R0, M[500]
inc R1, R0
store M[501], R1
R0
10 11
R1
PC=101
FetchDecode
Fetch Exec. ops
Store results
clk
store M[501], R1
Fetch Exec. ops
...
10
1.1..
Store results
clk
PC=102
FetchDecode
102

## Slide 38: Instruction Cycles
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
PC=100
FetchDecode
Fetch Exec. ops
Store results
clk
Registers
IR
PC
Memory
I/O
500
501
100 load cx, M[500]
inc dx, cx
store M[501], dx
cx
10 11
dx
PC=101
FetchDecode
Fetch Exec. ops
Store results
clk
store M[501], dx
Fetch Exec. ops
...
10
1.1..
Store results
clk
PC=102
FetchDecode
102

## Slide 39: Architectural Considerations
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
N-bit processor
  N-bit ALU, registers, buses, memory data interface
  Embedded: 8-bit, 16- bit, 32-bit common
  Desktop/servers: 32-
bit, even 64
PC size determines address space
Registers
IR
PC
Memory
I/O

## Slide 40: Architectural Considerations
Processor
Control unit
Datapath
ALU
Controller
Control
/Status
Clock frequency
  Inverse of clock period (f = 1/T)
  Must be longer than longest register to register delay in entire processor
  Memory access is often the longest
Registers
IR
PC
Memory
I/O

## Slide 41: Instruction Cycle State Diagram

## Slide 42: Advantages of High-Level Languages
Program development is faster
  High-level statements: fewer instructions to code
Program maintenance is easier
  For the same above reasons
Programs are portable
  Contain few machine-dependent details
    Can be used with little or no modifications on different machines
  Compiler translates to the target machine language
  However, Assembly language programs are not portable

## Slide 43: Why Learn Assembly Language?
Two main reasons:
  Accessibility to system hardware
  Space and time efficiency
Accessibility to system hardware
  Assembly Language is useful for implementing system software
  Also useful for small embedded system applications
Space and Time efficiency
  Understanding sources of program inefficiency
  Tuning program performance
  Writing compact code

## Slide 44: How a pipeline assembly code look like
Notes: http://www.mackido.com/Hardware/Pipelines.html is the image source

## Slide 45: How a pipeline assembly code look like
Notes: http://www.renesas.eu/support/faqs/faq_results/Q1000000-Q9999999/design/tech/tech_121gl.jsp is the image source